## Slide 1: Troubleshooting NLP schedule optimisation with OCV=f(SOC) 7th December 2018
Researcher: Diarmid Roberts
Supervisors: Dr. Solomon Brown, Prof. Andy Cruden, Dr. Rachael Rothman
Sponsor: Drax Power Ltd.

## Slide 2: Background
I have two versions of NLP schedule optimisation
  One assumes fixed OCV, based on figure of 1.46V at 50% SOC
  One makes OCV a linear function of SOC (and hence current in preceding sub-periods)
The example day I used in article looked reasonable – f(SOC) version gave very lightly worse revenue.
Across year f(SOC) returns £26.40/kW vs. fixedSOC £27.99/kW
Seems reasonable…

## Slide 3: Problem
I noticed that the difference in outputs varies significantly from day to day
Look at day where results differ lots:
Chart: Hour of Day 8th July 2017
NLP OCV50 | -233.1341 | -3.5897e-06 | 7.4575e-07 | 1298.0663 | 1910.131 | 172.6582 | 4.5725e-07 | -932.1677 | 956.0695 | 1.0518e-06 | -8.8282e-07 | 2.043e-06 | -185.2726 | -841.9987 | -761.3221 | -2722.6945 | -1615.1121 | 3200 | 3083.4872 | 3.7085e-05 | -3200 | -2129.6061 | 305.333 | 2019.1861
NLP_f_SOC | -217.3203 | -0.00018212 | 5.0527e-05 | 1316.7314 | 1944.1526 | 103.7523 | 4.642e-05 | -1249.6991 | 675.7277 | 0.00018716 | -208.9436 | 0.00019934 | -857.2085 | -1502.4833 | -1425.9766 | 6.7644 | -327.5486 | 3057.3368 | 2.0133 | 2100.9437 | -3200 | -2029.3259 | 284.0078 | 1937.6598
Price | 47.01 | 45.6 | 42.82 | 38 | 36.55 | 40.99 | 44.2 | 59.63 | 46.6 | 51.36 | 54.92 | 51.5 | 57.69 | 60.8 | 60.4 | 71.9 | 64.92 | 1.02 | 1.12 | 1.53 | 79.94 | 63.9 | 47.02 | 42.03
Why no discharge here in f(SOC) model?

## Slide 4: Problem
Although there’s no specific constraint on this behaviour in fixedOCV model, the solver always sets one variable to zero
This breaks down in the non-convex f(SOC) formulation
Chart: Hour of Day 16th Jan 2017
Charge current density | 1.9903e-05 | 6.9044e-06 | 8.5243e-05 | 1316.7314 | 1944.1526 | 103.7523 | 7.8773e-05 | 9.5665e-06 | 675.7277 | 0.00022816 | 0.00038977 | 0.00024281 | 0.00083306 | 0.0031387 | 0.0012437 | 3199.9992 | 1801.0373 | 3057.3368 | 2.0133 | 2100.9437 | 3.4415e-06 | 7.1007e-06 | 284.0078 | 1937.6598
Discharge current density | -217.3203 | -0.00018903 | -3.4716e-05 | -1.4312e-05 | -1.202e-05 | -2.2964e-05 | -3.2353e-05 | -1249.6991 | -1.4977e-05 | -4.1007e-05 | -208.9439 | -4.3469e-05 | -857.2093 | -1502.4864 | -1425.9779 | -3193.2348 | -2128.5858 | -2.4605e-06 | -2.4653e-06 | -2.4855e-06 | -3200 | -2029.3259 | -1.8977e-05 | -1.0642e-05
Problem is simultaneous charge and discharge!

## Slide 5: Problem
I checked the fixed OCV results, by correcting for actual OCV.
The error is low:
£27.99 becomes £28.40 across year
So fixedOCV version already gives good results